Constructing the Stabilizer

- Place all ribs on plan and cut spars, LE and TE to length.

- Cut LE sheet to length. Pic #2

Picture #1

- Cut  and glue the webbing to the bottom spar, adding a rib at a time.

- Glue TE sheeting to ribs. Clamp with clothes pins.

- Glue LE and diagonal root rib.

- Add bottom LE sheeting.

Picture #2

- Add diagonal brace from spar to diagonal root rib.

Picture #3

- Epoxy brass alignment tubes.  Add additional vertical webbing between LE sheeting and brass tubes. Pic #3

Picture #4

- Add cap strips to ribs, top and bottom.

- Add top sheeting.

- Sand to shape. Pic #5

Picture #5